Focal Lengths

focal ratio (f) = objective focal length (Fo) / diameter of the objective. (D)       f = FO / D

##### magnification = objective focal length (Fo)  / eyepiece focal length (Fe)    M = Fo / Fe

Relationship between the

Focal length (F)

object distance from the lens (do )

image distance from the lens (di)

1 / F    =    1 / do    +    1 / di

For objects very, very, very far away ….

1 / do    goes to zero

So …

1 / F    =    1 / di                or         F = di

Focal length = image distance

For a rough estimate

Measure the length from the objective to the end of the tube for a Newtonian, or to the position of the eyepiece, including diagonal, for a refractor

| Telescope | Type of Telescope Reflector/Refractor | Aperture | Rough Estimate of Focal Length |
| --- | --- | --- | --- |
| Bushnell (ball) telescope |  |  |  |
| Meade large telescope |  |  |  |
| Celestron tall four inch Newtonian |  |  |  |
| Solar telescope |  |  |  |
| Celestron long telescope with lenses |  |  |  |